## Slide 1: Chapter 1: Introduction

## Slide 2: Why use electrical energy?
Electricity delivers energy:
  Cleanly
  Efficiently
  Economically
  Flexibly

## Slide 3: What is its main drawback?
Storing large amounts of electrical energy is difficult or expensive
Electrical energy must be delivered as a continuous process
Rate of energy delivery i.e., power, is a fundamental concept
Reliable, continuous delivery requires coordinated operation of a set of devices i.e., a power system

## Slide 4: What are the attributes of a good power system?
Reliability
Economy
Sustainability
These objectives conflict:
  Improving reliability costs money
  Cheapest form of electricity generation are not always sustainable

## Slide 5: Physical structure of power systems
Multiple sources connected to multiple loads
Enhances reliability
  Single failure does not result in a loss of power to the consumers
Improves economy
  Aggregating loads reduces the amount of generation capacity needed
  Load can be supplied by most economical generation
Supports sustainability
  Aggregated wind and solar generation is less variable and more predictable

## Slide 6: Why ac?
Operating at higher voltages significantly reduces losses
Load

## Slide 7: Why ac?
Voltage | Relative Losses
110 V | 1
220 V | 0.25
13 kV | 71.6 10-6
132 kV | 694.4 10-9
345 kV | 101.7 10-9

## Slide 8: ac transformers
Step-up the voltage
Step-down the voltage
Relatively cheap
Highly reliable
Must balance
  Safety
  Cost
  Practicality
 Use different voltages at different locations

## Slide 9: Typical operating voltages in large power systems
Image: United States Department of Energy, Blackout 2003, “Final Report on the August 14, 2003, Blackout in the United States and Canada: Causes and Recommendations”
On average, only about 5% of the electrical energy generated in the United States is dissipated as losses in the transmission and distribution networks. Most of these losses occur in the low voltage distribution networks.

## Slide 10: Typical voltage levels
345 kV
132 kV
30 kV
11 kV
120 V
National
transmission
Regional sub-
transmission
Local
distribution
Street-level
distribution

## Slide 11: Typical consumer connections
345 kV
132 kV
30 kV
11 kV
120 V
Large
industrial
consumers
Industrial
consumers
Large
commercial
consumers
Residential and
commercial
consumers

## Slide 12: Transmission and distribution networks
Transmission network:
Transmit large amounts of power over long distances
Meshed network
Redundant paths:
  Improve reliability
  Improve economics
Requires sophisticated protection schemes against faults
Distribution network:
Distribute power to consumers over a limited area
Typically, radial network
  Except in some dense urban areas
Lower reliability
  Acceptable because faults affect fewer consumers
Radial networks require less sophisticated protection schemes against faults

## Slide 13: Centralized and distributed generation
Centralized generation
Conventional generation
  Coal plants
  Gas plants
  Hydro plants
  Nuclear plants
Renewable generation
  Wind farms
  Solar farms
Connected to the transmission network
Distributed generation
Rooftop solar panels
Connected to the distribution network

## Slide 14: What about high voltage dc transmission?
Requires power electronics
Convert high voltage ac into high voltage dc at one end of the line
Convert dc back into ac at the other end
These converter stations are very expensive
Justified when:
  A lot of power must be transmitted over a long distance
    Transmitting this power using ac could create stability problems
  Two power systems operating at different frequencies must be connected
  A long underground or submarine cable is required

## Slide 15: Cyber infrastructure
Control systems
Meters
Relays
Control centers
Communication networks
Computers

## Slide 16: Organizational structure
Traditional electric utility
  Owns and operates all the generation, transmission, and distribution assets
  Has a monopoly for the sale of electricity over its service territory
  Vertically integrated monopoly
  Investor-owned utilities are regulated by government body
Unbundled competitive market
  Generating companies compete to sell electrical energy in open market
  Transmission and distribution remain regulated monopolies
  System operator is responsible for reliability and efficient operation
  In some locations consumers buy electricity from their local distribution utility
  On other locations, they have a choice of supplier
More details in Chapter 12

## Slide 17: Historical evolution
Originally:
  Local generation supplying local consumers
  Mostly in urban areas
Economic and reliability benefits
  Development of transmission lines connecting remote generation to cities
  Interconnections between power systems
1930s: large scale rural electrification
1950s-1960s: development of continent-scale interconnections

## Slide 18: North-American interconnections
Source: Congressional Budget Office

## Slide 19: North-American interconnections

## Slide 20: Interconnected network of Continental Europe

## Slide 21: Worldwide interconnections
By Alinor at English Wikipedia, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=30154547

## Slide 22: Best renewable resources and largest load centers
Source: NREL

## Slide 23: Proposed United States supergrid
Source: NREL

## Slide 24: Proposed European supergrid
Emphasis on offshore wind

## Slide 25: Residential and commercial solar generation
Connected to the distribution network

## Slide 26: Microgrids
Image: MESA Solutions