## Slide 1: Chapter 2: Electrical Loads and the Demand for Electricity

## Slide 2: Simplified wiring diagram of a house
Load 1
Load 2
Load n
Loads are connected in parallel
  Within the house
  Across the power system
If the supply voltage remains relatively constant, we can add up the loads to estimate the total load.

## Slide 3: Quantifying loads
Loads are quantified
in terms of power,
not impedances
Appliance | Typical Rating
LED lightbulb | 9-15 W
Incandescent lightbulb | 60-100 W
Laptop computer | 65 – 100 W
Desktop computer | 250 – 500 W
Refrigerator | 300 – 1100 W
Single room air conditioner | 600 – 1500 W
Space heater | 750 – 1500 W
Water heater with tank | 2000 – 6000 W
Whole house air conditioner | 2500 - 4000 W
Electric shower | 8000 – 10000 W
Tankless water heater | 13000 – 36000 W

## Slide 4: Typical load profiles of residential consumers

## Slide 5: Typical load profiles of residential consumers

## Slide 6: Typical load profiles of residential consumers

## Slide 7: Power consumption profiles of fours houses, recorded every minute over the course of the same day

## Slide 8: Aggregated power consumption profile of 16 houses, recorded every minute over the course of the same day
Chart: Time of Day

## Slide 9: Summary data about the profiles of the four houses and the aggregation of the 16 houses
House | A | B | C | D | 16 houses
Peak load (kW) | 5.013 | 3.413 | 8.464 | 7.157 | 24.887
Minimum load (kW) | 0.045 | 0.083 | 0.141 | 0.179 | 2.454
Average load (kW) | 0.507 | 0.3027 | 0.7398 | 0.5747 | 6.985
Energy (kWh) | 12.171 | 7.264 | 17.754 | 13.794 | 167.633
Peak/average ratio | 9.88 | 11.27 | 11.44 | 12.45 | 3.56
Capacity Factor | 10.1% | 8.9% | 8.7% | 8.0% | 28.1%

## Slide 10: Aggregation
Suppose that each house installs its own generation
Must have sufficient capacity to meet its own peak load
16 houses separately  Need a total of 95 kW of generation capacity
Aggregation of 16 houses  Need only about 25 kW of generation capacity
Capacity factor:
Aggregation allows us to take advantage of the diversity in the demand of various consumers
Benefits of aggregation increase as we include more consumers and more consumer types

## Slide 11: Commercial consumer: “Education”

## Slide 12: Commercial consumer: “Retail”

## Slide 13: Commercial consumer: “Legal and Marketing”

## Slide 14: Commercial consumer: “Hotel Restaurant”

## Slide 15: Industrial Consumers
Wide variety of load profiles
Depends on the type of industry
  Process industries: (glass, aluminium, …)
    Fairly flat load because activity is constant
  Manufacturing industries:
    Depends on number of work shifts

## Slide 16: Aggregation over a large region
Example: MISO
42 million consumers

## Slide 17: Aggregated load profile for the MISO region Data recorded every 5 minutes on August 12, 2020
Chart: Time of Day
Peak load: 104,347 MW
Average load: 85,898 MW
Peak to average: 1.21

## Slide 18: Short-term effects on load profile
Astronomical factors
  Time of day
  Day of the week
  Time of the year
    sunrise, sunset, daylight saving time
  Holidays
Weather
  Temperature, cloud cover, wind, humidity
Special events
    Examples: television specials, other events
    Loss of load diversity

## Slide 19: Effect of temperature on electricity demand
Changes in the average and peak load as a function of the average daily temperature for the ERCOT and PJM systems.
Source: Maximilian Auffhammer et al. PNAS
doi:10.1073/pnas.1613193114 © 2017
by National Academy of Sciences

## Slide 20: Load profiles on the days with the highest and lowest loads in Great Britain
Maximum and minimum temperatures in London
December 15, 2022
  36°F (2°C)
  21°F (-6°C)
June 12, 2022
  81°F (27°C)
  55°F (13°C)
Chart: National Grid (Great Britain)
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.5 | 12 | 12.5 | 13 | 13.5 | 14 | 14.5 | 15 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.5 | 19 | 19.5 | 20 | 20.5 | 21 | 21.5 | 22 | 22.5 | 23 | 23.5 | 24
Thursday, December 15, 2022 | 28752 | 29425 | 29286 | 28494 | 28092 | 28210 | 27990 | 27807 | 27374 | 27392 | 27710 | 28778 | 31559 | 34212 | 37050 | 39050 | 41100 | 42138 | 43035 | 43097 | 42634 | 42198 | 41847 | 41265 | 41170 | 40987 | 40726 | 40666 | 40864 | 41044 | 41741 | 42920 | 44787 | 45700 | 46147 | 45964 | 45777 | 45173 | 44414 | 43742 | 42353 | 41143 | 39989 | 38233 | 35854 | 34070 | 31723 | 30503
Sunday, June 12, 2022 | 18271 | 17915 | 17239 | 17060 | 16525 | 16199 | 15933 | 15807 | 15557 | 15036 | 14879 | 15079 | 15465 | 15582 | 15850 | 16133 | 17341 | 17395 | 17886 | 18024 | 18351 | 18420 | 18913 | 18912 | 18982 | 18779 | 18348 | 17852 | 17639 | 17417 | 17395 | 17756 | 18529 | 19921 | 21077 | 22105 | 22712 | 23259 | 23448 | 23569 | 23627 | 23480 | 23156 | 22914 | 22821 | 21943 | 20475 | 19529
Data: NGCESO

## Slide 21: Load profiles on the days with the highest and lowest loads in Texas
Maximum and minimum temperatures in Austin
July 20, 2022
  103°F (40°C)
  74°F (23°C)
April 7, 2022
  76°F (24°C)
  42°F(6°C)
Chart: ERCOT (Texas)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Wednesday, July 20, 2022 | 59598.09 | 56757.49 | 54512.59 | 52789.52 | 51824.87 | 51892.46 | 52372.37 | 53090.23 | 55703.76 | 59441.89 | 63920.49 | 68574.3 | 72725.41 | 76154.81 | 78575.51 | 79618.5 | 80037.84 | 79772.08 | 78519.66 | 75943.21 | 73259.09 | 70798.71 | 67055.65 | 62805.51
Thursday, April 7, 2022 | 34378.07 | 32992 | 32200.91 | 31796.35 | 32227.98 | 34026.72 | 37289.72 | 38656.1 | 38863.29 | 39285.91 | 40006.47 | 40137.2 | 40306.4 | 40615.08 | 40826.68 | 41371.11 | 42105.86 | 42499.7 | 42121.09 | 41591.7 | 41787.73 | 40617.58 | 38237.43 | 35683.99
Data: ERCOT

## Slide 22: Effect of the total solar eclipse on demand 11th August 1999 on the load in Great Britain
Time
33000
33500
34500
35000
35500
36000
36500
09:00
09:10
09:20
09:30
09:40
09:50
10:00
10:10
10:20
10:30
10:40
10:50
11:00
11:10
11:20
11:30
11:40
11:50
12:00
12:10
12:20
12:30
12:40
12:50
13:00
Demand MW
Tue 10/08/1999
Wed 11/08/1999
Start of the
eclipse
End of the
eclipse
2200MW drop
in demand
3000MW
increase in
demand
Min @11:15
Max @11:44
Totality
34000
Data: National Grid

## Slide 23: Brazil vs. Chile June 24, 2010

## Slide 24: Long term effects on the demand
Historically:
  Consumption of electrical energy closely linked to economic activity
    Increase in commercial and industrial demand
    Household income grows  more appliances
Since 2000, growth in electricity demand is slower than the growth in Gross Domestic Product (GDP)
  Technological advances
    Use of power electronics
  Energy efficiency standards
    Buildings, appliances
  Structural shift in the economy
    Less manufacturing, more services

## Slide 25: U.S. electricity use growth rate
Source: Energy Information Agency – Annual Energy Outlook 2020
Chart: 
percentage growth
Three-year rolling average
AEO2022 economic growth cases
High Economic Growth
Reference
Low Economic Growth

## Slide 26: Electricity demand & economic activity
Source: NY Times

## Slide 27: Long term forecasts
Notoriously inaccurate
Often completely wrong
What factors make it even harder now?
  Decarbonization of the economy
    At what rate will transportation, heating be electrified?
  Effect of climate change
    Increased use of air conditioning
  Increase in “behind the meter” generation
    PV panels on residential rooftops

## Slide 28: US electricity use by end-use sector
Source: Energy Information Agency – Annual Energy Outlook 2020 - AEO2022 Reference case
Chart: TWh
| 1990 | 2021 | 2050 | 1990 | 2021 | 2050 | 1990 | 2021 | 2050 | 1990 | 2021 | 2050
Electric Sales | 924.0187 | 1490.3607 | 1814.8611 | 838.2631 | 1318.7407 | 1537.9532 | 945.5217 | 981.1542 | 1217.496 | 4.7512 | 12.9488 | 145.6831
Direct Use | 0.011772 | 28.4271 | 155.9852 | 2.5751 | 28.0249 | 94.2712 | 57.7159 | 114.0024 | 157.3836 | 0 | 0 | 0

## Slide 29: Effect of increasing amounts of behind-the-meter solar generation capacity on the shape of the system load for a typical spring day in New England
Source: ISO New England

## Slide 30: The California “Duck Curve”

## Slide 31: Metering and billing
Load 1
Load 2
Load N
Meter

## Slide 32: Electromechanical meter
Measures only energy consumed
Meter integrates mechanically the instantaneous active power
T: reading interval (typically one month)
No charge for reactive power

## Slide 33: “Smart” electronic meter
Digital rather than mechanical integration
Makes possible:
  Remote reading
  Remote disconnection
  Remote outage detection

## Slide 34: Electricity bill
Residential and small commercial consumers:
  : rate in $/kWh
  : fixed charge ($)
  : total amount
Larger commercial and industrial consumers:
  Fixed charge ($)
  Energy charge ($/kWh)
  Peak demand charge ($/kWpeak)
  Penalty for poor power factor
  Requires a more expensive meter

## Slide 35: Why charge for peak demand?
The cost to the utility of supplying electricity is not just a function of the energy delivered
The cost of the generating plants and the transmission and distribution networks is determined by the maximum amount of power that they have to produce or transmit.

## Slide 36: Example 2.1
Chart: Time of Day
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
 | 500 | 500 | 500 | 500 | 500 | 500 | 500 | 1000 | 1000 | 1000 | 2000 | 2000 | 500 | 1500 | 1500 | 1500 | 1500 | 500 | 500 | 500 | 500 | 500 | 500 | 500
This figure shows the load profile of an industrial consumer.
Calculate the electricity bill for this day assuming that it is charged 0.12 $/kWh for energy, that it pays 0.75 $/kW for its peak load and that the standing charge is $15.

## Slide 37: Example 2.1
Total energy consumed:
Peak load:
Daily electricity bill:

## Slide 38: Demand-side flexibility
Consumers expect to get power when they flip the switch
No energy storage  power produced must be equal to power consumed
Power generation must follow demand
Increasingly difficult and expensive as renewable generation increases
Can the demand be more flexible?
  Demand follows generation?
Time of use tariffs:
  Discourage consumption when generation is expensive
  Encourage consumption when generation is cheap

## Slide 39: Outages
Local outages
  Equipment failure
  Accidents
  Animals (squirrels, rats, crows,…)
  Storms, earthquakes, hurricanes
Wide-area outages (blackouts)
  Imbalance or instability in the system
Effect on individuals
  Health, life
  Inconvenience
Effect on businesses
  Economic losses

## Slide 40: Quantifying the cost of outages
Useful to estimate the value of countermeasures
Impact of an outage depends on:
  Vulnerability of individuals
    Elderly vs. college students
  Nature of the business
    Restart industrial process
  Timing of the outage
    Rush hour vs. middle of the night vs. super bowl Sunday
  Duration of the outage
  Geographical extent
A priori we can only get an estimated average cost

## Slide 41: Value of Lost Load (VoLL)
Estimated using surveys
“How much would you be willing to pay to avoid an unexpected outage?”
 Amount of money that an average consumer would be willing to pay to avoid not being able to consume a MWh of electrical energy

## Slide 42: Value of Lost Load in different regions
Country/Region | VoLL ($/MWh)
United Kingdom | $22,000
Countries of the European Union | $12,290 - $29,050
United States | $7,500
MISO | $3,500
New Zealand | $41,269
Victoria - Australia | $44,438
Australia | $45,708
Ireland | $9,538
Northeast USA | $9,283-$13,925
Spread of values illustrate how difficult it is to estimate VoLL
VoLL is about two order of magnitude greater than cost of energy
Shows that consumers value a reliable supply
Sources: London Economics, European Commission, Brattle Group, MISO. Where necessary, the values have been converted to US$

## Slide 43: Complex power
Lighting, heating loads  current in phase with the voltage
Other loads (e.g., motors)  current lags the voltage
Complex power:

## Slide 44: Active and reactive power
Active power:
Measures the rate at which electrical energy is consumed by the load and converted to another form of energy
Units: W, kW, MW
Reactive power:
Represents power that oscillates at twice the frequency of the voltage without being dissipated or put to practical use
Dimensionally similar to active power
Units: var (Volt Ampere reactive), kvar, Mvar

## Slide 45: Apparent power
The apparent power is the magnitude of the complex power:
Units: VA (Volt Ampere), kVA, MVA

## Slide 46: Power factor and power triangles
Lagging power factor:
Leading power factor:
Load “consumes”
reactive power
Load “produces”
reactive power

## Slide 47: Example 2.2: Complex power
A load is supplied by a 120 V source and draws a current of 5 A, which lags the voltage by 15°. Calculate the complex, active, reactive and apparent power supplied to this load, as well as its power factor.
lagging

## Slide 48: Example 2.3: Complex power
A load supplied from a 240 V source consumes 100 W of active power and 50 var of reactive power. Calculate the complex and apparent powers drawn by this load, as well as its power factor and the magnitude and phase of the current.
lagging

## Slide 49: Example 2.4: Complex power
A load supplied from a 440 V source consumes 200 W at a lagging power factor of 0.9. Calculate the complex, reactive and apparent powers drawn by this load, as well as the magnitude and phase of the current.

## Slide 50: Parallel loads
Meter
Load 1
Load n
Load 2

## Slide 51: Example 2.5: Parallel loads
Three loads are connected in parallel and supplied by an ideal 220 V voltage source:
: 200 W at unity power factor
: 400 W at 0.8 power factor lagging
: 300 W at 0.9 power factor leading
Calculate the total active power, reactive power, complex power, apparent power and current supplied by this source, as well as the power factor of the aggregated load.

## Slide 52: Example 2.5: Parallel loads (continued)

## Slide 53: Reactive power
Inductance forces the current to lag the voltage
   lagging power factor
Capacitance forces the current to lead the voltage
  leading power factor
Purely resistive load
  unity power factor:
  No reactive power
  All the current is put to practical use e.g., delivering active power
Power factors close to 1.0 are thus desirable
Large consumers are penalized if their power factor is lagging and too low
Residential meters do not measure reactive power

## Slide 54: Reactive power compensation
Meter
Load 1
Load n
Load 2
Lagging power factor
Improved power factor

## Slide 55: Example 2.6: Reactive power compensation
A load of 2 MW at 0.8 power factor lagging is supplied at 69 kV. Calculate the current that it draws from the source. Repeat this calculation for the case where this inductive load is compensated by a capacitive load of – 1 MVAr.
Uncompensated case:

## Slide 56: Example 2.6: Reactive power compensation
A load of 2 MW at 0.8 power factor lagging is supplied at 69 kV. Calculate the current that it draws from the source. Repeat this calculation for the case where this inductive load is compensated by a capacitive load of – 1 MVAr.
Compensated case:

## Slide 57: Reactive power compensation